ZIM.108.441.BOP

356/912 FUEL PUMP BLOCK OFF PLATE KIT

Often now people want to run an electric fuel pump on their 356 or 912 engine. We now manufacture this simple, but well designed block off plate, and we package it with the proper hardware to install it. It also includes an o-ring seal. No gasket required. You can, if you wish retain the use of your studs and use lock washers and nuts to retain the new block off plate, but we provide 2 hex head bolts, and 2 wave lock washers for a cleaner look. Recommended torque is 25 Lb Ft. Simply remove your old studs by double nutting them and removing them and use our included hardware to put it back. Make sure to install it properly on the case as it is Asymmetrical.  It will only work as designed in the proper direction. If you mount it backwards it will leak oil as the o-ring hangs off the edge of the cover and wont seal.

Dwb/z/2009 revised 8/2020